## Slide 1
Helios-Artemis
A Smarter Solar Controller for Rural Bangladesh
Hussain Touhid Siddiquee · Dept. EEE, Leading University Sylhet · 2026
1 / 10

## Slide 2
The Problem: Solar Power Wasted in Bangladesh Monsoon
2 / 10
6M+
rural households
have IDCOL solar panels
−15%
efficiency loss
during monsoon season
70.7%
actual tracking
efficiency in July storms
Why does this happen?
Solar panels have a 'sweet spot' voltage for maximum power. The standard controller (Perturb-and-Observe) finds this spot by trial-and-error — tiny voltage nudges back and forth. During clear weather this works fine. But during monsoon, clouds pass rapidly and the sweet spot keeps jumping. The controller is always reacting to the last cloud instead of anticipating the next one — so it wastes power.

## Slide 3
The Idea: Predict, Then Act
3 / 10
Old Way — React
☁ Cloud passes over panel
⚡ Power drops suddenly
🔁 Controller trial-and-errors its way back
⏱ Power wasted during recovery (can take seconds)
VS
Helios-Artemis — Predict
📡 Sensor reads current sky conditions
🧠 AI forecasts irradiance 30 min ahead
⚙️ Controller pre-adjusts voltage reference
✅ When cloud arrives — already at the right setting

## Slide 4
How It's Built: Two Chips, One Controller
4 / 10
🧠 HELIOS (ESP32-S3 chip)
THE BRAIN: Runs AI prediction
Looks at sky: Light sensor + camera
Forecasts irradiance: 30 minutes ahead
Updates every 100 ms: Sends voltage target to Artemis
Self-retrains: On-device, no internet needed
100 ms
UART
⚙️ ARTEMIS (STM32 chip)
THE MUSCLE: Handles real power control
Switches 50,000×/sec: Pulses current to extract power
Charges battery: 3-stage: bulk → absorb → float
Blends AI + logic: (1−α)×P&O + α×prediction
Real-time only: No AI inference here — no jitter

## Slide 5
The AI Component: What the LSTM Actually Does
5 / 10
Long Short-Term Memory (LSTM)
A type of neural network that learns patterns in sequences over time
Like how you can tell a storm is coming from an hour of darkening sky — not just the last second
Trained on 1 year of synthetic Sylhet irradiance data
Predicts irradiance 30 minutes ahead with R²=0.917
Only 4,486 parameters — tiny enough to run on a microchip in under 12 milliseconds
Retrains itself every 14 days using the controller's own logged data
MODEL SPECS
Architecture
32-unit LSTM, 1 layer
Input
24 hours of irradiance history
Output
Predicted GHI in 30 minutes
Parameters
4,486 total
Accuracy (R²)
0.917
Error (MAE)
50.7 W/m² daytime
Inference time
< 12 ms on the ESP32-S3
Retraining
Every 14 days, no internet

## Slide 6
Testing Method: Why Simulation?
6 / 10
Why simulate first?
Building hardware in Sylhet takes months (PCB fab, procurement, field site)
Simulation allows testing 30+ different days, 200 Monte Carlo runs, dozens of parameter sweeps — impossible and expensive in hardware
The simulation is built from NASA and SREDA real climate data for Sylhet — not arbitrary values
How realistic is the simulation?
Cloud patterns from real Sylhet climate records (NASA POWER + SREDA)
Sub-second cloud flicker modelled mathematically (calibrated from peer-reviewed measurements)
Includes dust on panels, sensor noise, haze — not ideal clean conditions
Simulated P&O efficiency (86.8%) matches field data from Hossain et al. within 1.8%
The simulation is more severe than real field conditions — so the performance gains reported are a conservative lower bound.

## Slide 7
7 / 10
Key Results
30-day Monte Carlo simulation — Sylhet July monsoon conditions
94.0%
Efficiency
(Helios-Artemis)
+23.3 pp
Gain over
standard P&O
0.917
AI forecast
accuracy (R²)
1,500 BDT
Controller cost
(USD ~14)
Method | Clear Sky | Monsoon | Annual Mean
Standard P&O | 86.8% | 70.9% | 85.8%
Variable-Step P&O | 90.5% | 78.3% | 89.1%
Incremental Cond. | 89.2% | 75.2% | 87.7%
★ Helios-Artemis | 93.2% | 95.1% | 91.3%

## Slide 8
Cost & Real-World Impact
8 / 10
Cost Comparison
Chart: 
| Commercial MPPT Controller | Helios-Artemis (this work)
Cost (BDT) | 13500 | 1500
89% cheaper than commercial alternatives
~6 Million
households could benefit from this upgrade
+4.8 kWh/yr
extra energy per 50W panel
5.2 years
payback period (vs plain P&O baseline)
Zero internet
required — fully offline operation

## Slide 9
Honest Limitations & Next Steps
9 / 10
⚠ Current Limitations
All results come from simulation — no real hardware built yet
The AI's 30-min forecast has a margin of error (~50 W/m²)
Simulation is conservative but not validated with real Sylhet sensors
Battery degradation and long-term reliability not yet modelled
✅ Immediate Next Steps
Q3 2026
Build hardware prototype in Sylhet
Field test
Compare simulated vs real efficiency under identical conditions
MOSFET upgrade
IRFB4110 MOSFET (86% less heat loss)
Journal sub.
MDPI Energies, after hardware validation

## Slide 10
In Summary
The Problem
6M+ Bangladeshi rural homes lose 15% of solar energy every monsoon because standard controllers can't keep up with fast-moving clouds.
The Solution
Helios-Artemis uses a small AI (LSTM) on an ESP32 chip to predict irradiance 30 min ahead, letting the controller pre-adjust instead of react.
The Results
Monsoon efficiency improves from 70.7% to 94.0% — a +23.3 pp gain. Controller costs ~1,500 BDT, 89% below commercial alternatives.
The Limit
These are simulation results. Hardware prototype and field trial in Sylhet is the confirmed next step (Q3 2026).
Thank you · Questions welcome
10 / 10