## Slide 1
Helios-Artemis
Dual-MCU Predictive MPPT Controller
Design and Simulation-Based Validation for Sylhet Monsoon SHS Deployment · Bangladesh
Hussain Touhid Siddiquee · Dept. of EEE, Leading University Sylhet · 2026
94.0%
Monsoon Efficiency
+23.3 pp
Gain vs P&O
~1,500 BDT
Controller Cost
89% ↓
vs Commercial
1 / 14

## Slide 2
CONTEXT & PROBLEM
The Monsoon Yield Gap in Bangladesh Solar
IDCOL SHS Programme — 6 million rural households affected
Bangladesh's IDCOL Solar Home System programme electrified 6M+ rural households — the world's largest off-grid solar programme. Yet MPPT efficiency is the #1 cause of yield shortfall every monsoon season (June–September).
6M+
Rural households
IDCOL SHS programme
70.7%
July monsoon efficiency
Min. single-day P&O
−15.1pp
Efficiency shortfall
vs clear-sky 86.8%
Why Standard P&O Fails in Monsoon
Reactive paradigm: P&O only responds AFTER irradiance has changed — always one step behind.
Cloud transients: Sylhet monsoon brings sub-second irradiance swings up to ±25% (σ = 25%, Ornstein-Uhlenbeck calibrated).
Perturbation mismatch: When a cloud shadow arrives mid-perturbation, the controller steps the wrong direction, wasting energy during recovery.
Scale of loss: 15.1 percentage-point drop = significant annual kWh loss across 6M homes and accelerated battery wear.
2 / 14

## Slide 3
ARCHITECTURE
Dual-MCU Architecture: Helios + Artemis
Functional decoupling of AI inference from real-time power control
HELIOS (ESP32-S3)
240 MHz dual-core, 512 kB SRAM
Brain: Edge AI processor
LSTM inference < 12 ms
32-unit model, 4,486 params
TSL2591 light sensor + OV2640 camera
Sky condition input
100 ms UART → sends V_MPP_pred to Artemis
Communication bridge
TF.js on-device retraining
14-day silent cycles, zero cloud
SD logging + browser dashboard
Monitoring & data capture
100 ms UART
←→
ARTEMIS (STM32F103)
72 MHz Cortex-M3, 20 kB SRAM
Muscle: Real-time power controller
50 kHz PWM — IRFB4110 via TC4420
Buck converter switching
Variable-step P&O every 100 ms
MPPT algorithm (reactive)
V_ref = (1−α)·V_P&O + α·V_pred
LSTM blend formula
INA219 12-bit I²C, 0.1Ω shunt
Battery current/voltage monitor
3-stage CC/CV charging
Bulk 6A → Absorb 14.7V → Float 13.8V
3 / 14

## Slide 4
ARTEMIS — POWER STAGE
Variable-Step P&O and Buck Converter Design
STM32F103 real-time control — 50 kHz switching, adaptive step sizing
Variable-Step P&O Algorithm
Step size law:
dV = clip(0.008 · |dP/dV|, 0.05, 0.60) V
Cold-start convergence:
~18 steps to 94% of MPP
Steady-state oscillation:
Low — step floors at 50 mV
Prediction blend:
V_ref = (1−α)·V_P&O + α·V_MPP,pred
Blend deadband:
|Ĝ−G|/G > 15% — suppresses spurious blends
Cloud-clearing α:
0.45·exp(−1.5·rel_dev) [higher trust]
Cloud-drop α:
0.08·exp(−1.0·rel_dev) [conservative]
Post-blend cooldown:
20 steps before next blend event
Buck Converter & Battery Charging
MOSFET
IRFB4110 — VDS 60V, RDS(on) 28 mΩ
Gate Driver
TC4420 — 50 kHz PWM
Inductor
100 μH
Capacitor
470 μF
Current Sense
INA219 — 12-bit, I²C, 0.1Ω shunt
Sensor noise
σ_I = 2 mA, σ_V = 10 mV
3-Stage CC/CV Charging Profile
Bulk
6 A until 14.7 V
Absorption
14.7 V until I < 0.5 A
Float
13.8 V maintenance
4 / 14

## Slide 5
HELIOS — LSTM AI
Dual-LSTM Architecture on ESP32-S3
Irradiance forecaster + gain scheduler — TinyML for edge deployment
Model Architecture & Specifications
Model 1 — Irradiance Forecaster
Units:
32 LSTM units, 1 layer
Input:
24-hr normalised GHI lookback (288 steps × 5-min)
Output:
30-min ahead GHI prediction
Params:
4,385
Inference:
< 12 ms float32 on ESP32-S3
Model 2 — Gain Scheduler
Units:
4 LSTM units, 1 layer
Output:
Optimal P&O step scaling factor
Params:
101 (total dual-model: 4,486)
Performance & Deployment
R² = 0.917
Year-2 independent test set
MAE 50.7 W/m²
Daytime forecast error
RMSE 63.6 W/m²
Root mean square error
Residual bias μ = +2.3 W/m² — slight positive bias means no systematic under-prediction → voltage reference never under-positioned.
Int8 Quantisation Option
4.7 ms vs 12 ms float32 — ΔR² = −0.009. Float32 retained to preserve fidelity within 100 ms UART budget.
5 / 14

## Slide 6
SIMULATION MODEL
Calibrated Sylhet Markov+OU Irradiance Model
Four physical realism layers — parameterised from NASA POWER & SREDA data
R1 — Sub-Second OU Flicker
Ornstein-Uhlenbeck process: τ = 1s, σ = 25%
Calibrated from Lave & Kleissl (2010) Colorado dataset
Models rapid cloud-edge irradiance fluctuations
Peak modelled GHI: 744 W/m² (July, aerosol-capped)
R2 — Aerosol / Haze Attenuation
Linke turbidity TL ≈ 4.5 (tropical humid)
Multiplicative factor ×0.93 on clear-sky GHI
Matches Sylhet seasonal haze patterns
Reduces clear-sky peak from 800 to ~744 W/m²
R3 — ADC Sensor Noise
INA219 current noise: σ_I = 2 mA
Voltage noise: σ_V = 10 mV (incl. switching EMI)
Added to measurement inputs, not true MPP signal
Tests MPPT robustness under realistic conditions
R4 — Panel Soiling
3% reduction on Isc (short-circuit current)
Monthly cleaning cycle modelled
Reflects realistic rural deployment maintenance
Small but cumulative efficiency effect
Sylhet Monthly Parameters (NASA POWER + SREDA)
6 / 14

## Slide 7
SIMULATION MODEL
Sylhet Monthly Irradiance Parameters
Parameterised from NASA POWER Level 3 data + SREDA Bangladesh Solar Atlas
Parameter
Jan
Apr
Jul
Sep
Oct
Dec
Peak GHI (W/m²)
820
880
580
650
780
800
Cloud Variability Index
0.15
0.30
0.85
0.65
0.30
0.15
Sunrise (hh:mm)
06:18
05:36
05:18
05:48
06:00
06:24
Sunset (hh:mm)
17:24
18:36
19:06
18:12
17:36
17:06
Daylight Hours
11.1
13.0
13.8
12.4
11.6
10.7
July is the most challenging month: Cloud Variability Index (CVI) = 0.85 — highest cloud transient frequency. Peak GHI drops to 580 W/m² (vs 880 W/m² in April) due to cloud cover AND aerosol loading. This is where the 23.3 pp efficiency gain of Helios-Artemis over plain P&O is most pronounced.
PV Model: Exact analytical MPP solution Vmp_c = Voc_T · (1/(1+k))^(1/k) ensures Ppv/Pm ≈ 1.00 at perfect tracking. 50 Wp mono-Si: Isc₀=2.91A post-soiling, k=14.26.
7 / 14

## Slide 8
RESULTS — LSTM
LSTM Predictor: Year-2 Independent Evaluation
Model trained on Year-1; evaluated on Year-2 with distinct random seed — no data leakage
R² = 0.917
Coefficient of Determination
Year-2 test set (365 days)
50.7 W/m²
Daytime MAE
Mean Absolute Error
+2.3 W/m²
Residual Bias
Slight positive — no under-prediction
LSTM Architecture Ablation Study
Architecture
R²
MAE (W/m²)
RMSE (W/m²)
Inference
Params
16 units, 1 layer
0.858
67.1
83.3
~6 ms
~1,900
32 units, 1 layer ✓
0.917
50.7
63.6
12 ms
4,385
64 units, 1 layer
0.934
45.0
56.6
~37 ms
22,849
✓ Selected — optimal Pareto point: best R² within 12 ms inference budget
α Sensitivity Analysis
α < 0.20
Under-blend zone
LSTM under-weighted
0.8–2.5 pp gain only
α 0.20–0.55
Stable plateau ✓
Optimal operation
5.5–6.2 pp clear, 23.6–24.4 pp monsoon
α > 0.60
Over-blend zone
LSTM errors dominate
efficiency falls
Optimal α = 0.35 · Plateau Δα = 0.35 · Robust to ±50% variation
8 / 14

## Slide 9
RESULTS — MPPT
MPPT Tracking Efficiency: Full Comparison
Monte Carlo N=30 — Sylhet parameterised conditions
94.0%
Monsoon efficiency
30-day Monte Carlo mean
±0.6%
Std deviation
σ across 30 July days
+23.3pp
Gain over P&O
70.7% → 94.0%
91.3%
Annual mean
Weighted across seasons
Full Efficiency Table — All Scenarios and Methods
Scenario
Plain P&O
Variable-Step P&O
Incremental Cond.
★ Helios-Artemis (this work)
Gain vs P&O
Clear Day (Jan)
86.8 ± 1.7%
90.5 ± 1.5%
89.2 ± 1.7%
93.2 ± 1.1%
+6.4 pp
Monsoon (Jul) ⚡
70.9 ± 3.8%
78.3 ± 3.4%
75.2 ± 3.8%
95.1 ± 2.1%
+24.2 pp
Partial Shading
85.6 ± 2.4%
89.0 ± 2.0%
87.5 ± 2.1%
93.3 ± 1.6%
+7.7 pp
Annual Mean
85.8 ± 1.5%
89.1 ± 1.2%
87.7 ± 1.3%
91.3 ± 1.0%
+5.5 pp
95% CI (July, 30-day Monte Carlo): [92.9%, 94.9%] — All 30 days within 90–95% efficiency band
9 / 14

## Slide 10
RESULTS — FULL-DAY SIM
Representative July Day Simulation (Seed 23)
Six key telemetry channels — Sylhet monsoon worst-case conditions
Irradiance (GHI)
Peak 744 W/m²
Aerosol-capped; sub-second OU flicker active
P_PV vs P_MPP
94.0–95.7%
Power extracted / theoretical max
η_MPPT Tracking
94.0% mean
30-day Monte Carlo range
Battery SoC
45% → 100%
Full charge in 13-hr Sylhet July window
Battery Voltage
12.41 – 13.61 V
CC/CV profile: bulk → absorb → float
Junction Temp T_J
Peak 62 °C
35°C ambient, Rth_JA ≈ 13.5°C/W, ~2W peak loss
Key validation: SoC reaches 100% within the 13-hour July solar window — confirms energy balance of controller design under maximum monsoon variability. Full charge from 45% initial state.
10 / 14

## Slide 11
VALIDATION
Validation vs Hossain et al. Field Baselines
Partial simulation-to-field cross-validation (IDCOL SHS field-measured data)
Clear-Sky Validation (January)
Hossain et al. field range:
79 – 85% plain P&O (field-measured)
Simulated P&O (this work):
86.8% ± 1.7% (Monte Carlo)
Match within +1.8 pp of field upper bound — model over-performs slightly vs field (conservative)
Projected Helios-Artemis clear-sky: 93.2 ± 1.1% → +6.4 pp above field maximum
Monsoon Validation (July)
Hossain et al. field range:
79 – 85% plain P&O (field-measured)
Simulated P&O (this work):
70.7% ± 3.8% (Monte Carlo)
8.3 pp below field lower bound. Attributed to Sylhet Markov+OU sub-second flicker (σ=25%) being more severe than monthly-averaged field variability in Hossain et al. This conservative monsoon estimate STRENGTHENS the case for Helios-Artemis.
Projected Helios-Artemis monsoon: 95.1 ± 2.1% → +16.8 pp above field minimum
11 / 14

## Slide 12
COST-BENEFIT
Cost Analysis and Economic Impact
Component BOM vs IDCOL-compatible commercial alternatives — Q1 2026 Dhaka retail
Bill of Materials (BOM)
ESP32-S3 (Helios MCU)
380 BDT
25%
STM32F103 (Artemis MCU)
120 BDT
8%
INA219 current sensor
80 BDT
5%
TSL2591 light sensor
120 BDT
8%
Buck converter passives
350 BDT
23%
PCB and housing
280 BDT
19%
Misc. connectors
170 BDT
11%
TOTAL CONTROLLER COST: ~1,500 BDT (≈ USD 14)
Economic Impact
Commercial IDCOL-compatible MPPT:
~13,500 BDT (≈ USD 122)
Helios-Artemis controller:
~1,500 BDT (≈ USD 14)
89% cost reduction — saves ~12,000 BDT per unit
Annual efficiency gain
+4.8 kWh per 50 Wp panel
Rural avoided cost
60 BDT / kWh
Annual energy value
+289 BDT / year
Payback period
~5.2 years vs plain P&O
Scale: 6M households × 289 BDT/yr = ~1.73 Billion BDT annual energy value unlock
12 / 14

## Slide 13
LIMITATIONS & ROADMAP
Honest Limitations and Research Roadmap
Simulation-based validation — hardware prototype and field trial are the immediate next step
Known Limitations
Simulation-only: Zero hardware measurements collected. All efficiency figures derived from calibrated Sylhet Markov+OU model.
LSTM forecast error: MAE = 50.7 W/m² daytime — meaningful uncertainty in transient prediction accuracy.
Sim-to-hardware fidelity: Blend formula efficiency gain (vs pure VS-P&O) not empirically confirmed on real hardware.
Battery degradation: Long-term cycle life, SoC drift, and capacity fade not modelled in this study.
Year-2 R² = 0.917: Lower than comparable cloud-connected LSTM papers (R²≈0.95+) — reflects Sylhet climate difficulty, not model weakness.
Research Roadmap
Q3 2026
Hardware Prototype (Sylhet): Fabricate PCB, procure IRFB4110 (RDS(on) 3.7 mΩ).
Q3 2026
Field Deployment: Deploy at rural SHS site in Sylhet. Collect real-sensor irradiance for LSTM training data.
Q4 2026
Empirical Comparison: Measure real vs simulated MPPT efficiency under identical irradiance — validate Markov+OU model fidelity.
Q1 2027
Journal Submission: Target: MDPI Energies. Hardware-validated results with full methodology.
Future
Scale & Expansion: Multi-panel MPPT, partial shading optimisation, IRFB4110 thermal analysis, wider Bangladesh rollout.
Simulation code & figure generation: github.com/touhidsiddiqueeraj-bit/artemis-helios
13 / 14

## Slide 14
Conclusions
6M households
IDCOL SHS programme — monsoon P&O tracking gap directly reduces household energy access & battery cycle life.
Dual-MCU decoupling
ESP32-S3 (Helios) handles LSTM inference without introducing jitter into STM32F103 (Artemis) 50 kHz control loop.
R² = 0.917 predictor
Year-2 independent test, 50.7 W/m² MAE. Lower than cloud-connected models — reflects Sylhet difficulty, not model failure.
+23.3 pp monsoon gain
70.7% → 94.0% (Monte Carlo); robust plateau α ∈ [0.20, 0.55] resolves overfitting concerns.
1,500 BDT controller
89% below commercial alternatives. ~5.2-year payback vs plain P&O at rural 60 BDT/kWh avoided cost.
Next: hardware & field
Q3 2026 Sylhet prototype. IRFB4110 MOSFET upgrade (−86% conduction loss). Then journal submission.
Thank you · Hussain Touhid Siddiquee · Dept. EEE, Leading University Sylhet · 2026
14 / 14